## Slide 1
IMPLANTABLE MICROELECTRONIC DEVICE:
DESIGN AND TEST OF MICROELECTRONIC DEVICE FOR OPTOGENETIC APPLICATIONS

## Slide 2: 1. OVERVIEW OF THE PROJECT
Restrictions
Low power device
(Just to supply a LED)
Wireless Power
(Magnetic coupling power harvesting)
Flexible substrate
(must be adaptable to the Surface)
Biocompatibility
(encapsulation is crutial)
Purpose of the project
Microelectronic Device
Optogenetics Technique
Wireless Power Supply
Lim, D. H., & LeDue, J. (2017) What Is Optogenetics and How Can We Use It to Discover More About the Brain?. Frontiers for young minds.

## Slide 3: 2. PREVIOUS SIMILAR WORKS
John Rogers’ Research Group  Different designs from the most simple to “higher” complexity.
1
2
3
In their work Fully implantable optoelectronic systems for battery-free, multimodal operation in neuroscience research (2018) in Nature Electronics:

## Slide 4: 2. PREVIOUS SIMILAR WORKS
John Rogers’ Research Group  Different designs from the most simple to “higher” complexity.
Mickle, A. D., Won, S. M., … Rogers, J.(2019). A wireless closed-loop system for optogenetic peripheral neuromodulation. Nature, 565(7739), 361.
In their work A wireless closed-loop system for optogenetic peripheral neuromodulation (2019) in Nature:

## Slide 5: 2. PREVIOUS SIMILAR WORKS
John Rogers’ Research Group  Different designs from the most simple to “higher” complexity.
In their work Fully implantable optoelectronic systems for battery-free, multimodal operation in neuroscience research (2018) in Nature Electronics:
Substrate: Pyralux AP8535R, a flexible substrate for bioimplantable devices.
Microcontroler (µC ): ATtiny84(Atmel)  many documentation available.
LDO: NCP161 ON semiconductor  Good specs. for low power device.
Cree® TR2227™ LEDs 3.15 V and 20mA.
Other passive components: 0201 and 0402 package size.
Accesibility to the µC: just once before the surgery.
Temperature of the implant due to the µC performance.
Biocompatibility problema when adding a µC in an implant (soldering components, resins, etc)
Technical Features
Possible Problems

## Slide 6: 2. PREVIOUS SIMILAR WORKS
Ada Poon’ Research Group  Simple design with a magnetic coupling.
Ho, J. S., Tanabe, Y., Iyer, S. M., Christensen, A. J., Grosenick, L., Deisseroth, K., ... & Poon, A. S. (2015). Self-tracking energy transfer for neural stimulation in untethered mice. Physical Review Applied, 4(2), 024001.

## Slide 7: 2. PREVIOUS SIMILAR WORKS
Ada Poon’ Research Group  Simple design with a magnetic coupling.
Technical Features
Possible Problems
Magnetic Coupling: Three turn coil with SMD capacitor (4pF) and resonant frequency of 1.5GHz.
Power consumption: approximately 4W.
Designed for only 1 or more leds working at the same pulse.
No control structure implemented.
Usage of non biocompatible-flexible substrate.

## Slide 8: 3. IDEAS FOR IMPROVEMENT
Using a microcontroller inside the brain increases the size of the implant so far.
For more that one µILED they used a µC  What about using different frequencies for powering different µILEDS?
Fixed antenna with helmet or subdermal implant on the patient.
Poon’s device  improve substrate, technical characteristics (Using CREE LED) and improving the power management on the circuit (Light intensity of the LE, temperature, power consumption, etc).
Problems found

## Slide 9: 3. IDEAS FOR IMPROVEMENT
Next Steps
1. Learn about magnetic coupling
2. Run a test with the Ada Poon’s Proposed Circuit
1 week
2 weeks
1 weeks
3. Run a test with the John Rogers Proposed Circuit
Check my repository on github and share your info: https://github.com/GGChe/BioImplantableDevice